High-Performance, Non-Yellowing, Penetrating Masonry and Stone Sealer: Dri-Look micronized polymer sealer by Concrete Coatings Inc. A light coating of sealer will provide an invisible barrier for brick, manufactured and natural stone surfaces. Use on masonry, manufactured and natural stone surfaces to provide protection and extend the life of these surfaces.

Sealer dries to a matte or natural finish, penetrates the surface to repel water and natural elements. Our Dri-Look sealer can be used on interior or exterior masonry, manufactured and natural stone.

SECTION 040140

MASONRY AND STONE SEALERS

PART 1	GENERAL

1.1	SUMMARY

A.	This section specifies a supplied sealer for vertical masonry or stone surfaces.

B. 	Related sections: Refer to the following specification sections for coordination.

1. 	Section .

1.2	SUBMITTALS

A.	Product Data: Submit manufacturer's product data and installation instructions.

B	Mock-Up:  Prepare a test area minimum 2 by 2 feet in size to verify suitability of the sealer and final appearance.

1.3	QUALITY ASSURANCE

A. 	Manufacturer: Minimum 5 years of experience in masonry and stone installation.

B.	Installer:  Licensed installers, experienced and trained in the use of specified products.

C.	Suitability of Substrate:  Do not apply to dirty or contaminated surface.  Surface must be clean and dry before application.

D.	Regulatory Requirements: Comply with requirements of authorities having jurisdiction and applicable codes at the location of the project.

1.4	DELIVERY, STORAGE AND HANDLING

A.	Deliver materials and products in unopened factory labeled packages. Protect from damage.

B. 	Store in a safe place, out of direct sunlight and away from heat.  Keep containers tightly sealed.  Do not allow product to freeze.  Use within manufacturer’s recommended shelf life, 12 months.

PART 2 - PRODUCTS

2.1	MATERIALS

- High-Performance, Non-Yellowing, Penetrating Masonry and Stone Sealer:  CCI Dri-Look micronized polymer sealer by Concrete Coatings Inc., 1105 North 1600 West, Layton, UT 84041, 800-443-2871, www.concretecoatingsinc.com. Provide the following:

  - Sealer: Dri-Look

  - Performance

    - Water Resistance

    - Invisible Finish

    - Interior/Exterior Use

    - No Odor or Silicone

    - Coverage: As recommended by manufacture

PART 3 - EXECUTION

3.1	INSPECTION AND PREPARATION

A.	Inspection:  Prior to start of application, inspect existing conditions to ensure surfaces are suitable for installation including the following:

1.	Grout has cured for a minimum of 14 days prior to application of sealer.

2.	Surface is completely free of dirt, paint, alkali, foreign materials that would prevent the sealer from penetrating the sealer to the surface.

3.	Area is completely dry.

4.     Test has been approved.

3.2	APPLICATION

A.	Masonry Sealer:  Strictly comply with manufacturer’s installation recommendations including the following.

1.	Clean surface as recommended by manufacturer.

2.	Apply at rate recommended by manufacturer.

3.	All surfaces designated as being sealed in the plans and specification shall be sealed with one even coat of Dri-Look sealer at the rate of approximately 600 square feet per gallon.

3.3	CLEAN & PROTECTION

A.	Protection:  Do not cover, but protect area from paint and other contaminates that could inhibit the sealer from penetrating and adhering.

END OF SECTION